## Slide 1: CPAP
Mike Callihan RN,BSN, Paramedic, EMSI
Miami Valley Hospital
EMS Education

## Slide 2: Objectives
Define Congestive Heart Failure
Define COPD
Review standing orders for CHF and COPD
Describe CPAP
Practice usage of CPAP

## Slide 3: A congested heart

## Slide 4: Congestive Heart Failure
Congestive Heart Failure (CHF) is a serious disease associated with excessive morbidity and mortality and of elevated health-care costs.
Even with the advances in pharmacologic therapy, the mortality for the disease remains very high.

## Slide 5: Congestive Heart Failure
Approximately 80% of patients with CHF showed restrictive spirometric pattern
Extravascular volume expansion and fluid accumulation in interstitial compartments of the lungs
Fluid accumulation is associated with increased heart size and reduced lung compliance.

## Slide 6: Congestive Heart Failure
The accumulation of fluid leads to flooding of the alveoli resulting in a deficiency in gas exchange with several consequences,
  Muscle weakness
  Dyspnea with routine activities.
  Dyspnea progresses into dyspnea at rest.

## Slide 7: Bronchioles and Alveoli
Deoxygenated
Blood
from the Heart
Pulmonary
Arteriole
Oxygenated Blood
to the Heart
Pulmonary
Venule
Bronchus
Bronchiole
Alveoli
Smallest Blood
Vessels
(Capillaries)
Notes: Bronchioles and Alveoli are part of the lower airway. Point out the flow of blood.
Point out the Pulmonary Vein is the only vein in the body that carries oxygenated blood and the Pulmonary Artery is the only artery to carry Unoxygenated (Bad) blood
Alveoli is where gas exchange takes place. There are ~300 million, and are incased in the pulmonary capillaries – where gas exchange takes place
Bronchioles act as both a conducting airway and gas exchange area

## Slide 8: Pulmonary Edema Protocol
Assess for
  Cyanosis
  clammy skin
  absence of fever
  coughing
  wheezing, labored breathing
  pitting edema
  rales in bilateral lower fields
  tachypnea
  apprehension
  JVD
  Inability to talk.

## Slide 9: Treatment
If CPAP is available, its use is encouraged prior to initiation of drug therapy
If SBP>100, NTG 0.4 mg SL up to 3, 1 every 5minutes. Maintain SBP > 100
Furosemide 80 mg slow IV push over 2 minutes. Maintain SBP >100
Morphine, up to 5 mg, Slow IV over 2 minutes. Maintain SBP > 100. May repeat morphine, up to 5 mg, slow IV over 2 minutes.

## Slide 10: Pulmonary Edema

## Slide 11: COPD
COPD, or chronic obstructive pulmonary disease, is a progressive disease that makes it hard to breathe.
"Progressive" means the disease gets worse over time.
COPD can cause coughing that produces large amounts of mucus (a slimy substance), wheezing, shortness of breath, chest tightness, and other symptoms.

## Slide 12: COPD
Airways and air sacs are elastic
In COPD, less air flows in and out of the airways because of one or more of the following:
  The airways and air sacs lose their elastic quality.
  The walls between many of the air sacs are destroyed.
  The walls of the airways become thick and inflamed (swollen).
  The airways make more mucus than usual, which tends to clog the airways.

## Slide 13: COPD
COPD can cause:
  coughing that produces large amounts of mucus,
  wheezing
  shortness of breath
  chest tightness
  other symptoms.

## Slide 14: COPD causes
Cigarette smoking is the leading cause of COPD. Most people who have COPD smoke or used to smoke.
Long-term exposure to other lung irritants, such as air pollution, chemical fumes, or dust, also may contribute to COPD.

## Slide 15: Asthma/Emphysema/COPD
Consider albuterol 2.5 mg and ipratropium 0.5 mg, nebulized with O2 8-12 LPM.
May repeat Albuterol 2.5 mg nebulized X 2.
COPD, CPAP or BiPAP
If patient arrests, tension pneumothorax is a likely cause
For asthmatics in severe distress: Epinephrine (1:1000) .3 mg SQ or autoinjector.
With Med control approval, may repeat Epinephrine.

## Slide 16: So what is CPAP?

## Slide 17: CPAP
Continuous positive airway pressure
CPAP is a tool to be used for assisting ventilation and should not be confused with trying correct Oxygenation concerns

## Slide 18: Indications
  Medical history and presenting complaints consistent with pulmonary edema
  Patient must be 16 or older
  COPD, Asthma
  Bibasilar or diffuse rales
  Near drowning
  Disasters or mass casualties such as Bioterrorism with cases of respiratory distress

## Slide 19: Contraindications
Respiratory or cardiac arrest
Agonal respirations
Severely depressed level of consciousness
Systolic blood pressure < 90mmHg
Signs and symptoms of pneumothorax
Inability to maintain airway patency
Major trauma, especially head injury with increased ICP or significant chest trauma
Facial Anomalies, e.g., burns, fractures
Vomiting
If patient deteriorates while on CPAP (O2 sats < 90), then prepare to intubate

## Slide 20: Hazards of CPAP
Hypotension
Pneumothorax
Corneal Drying

## Slide 21: Benefits to CPAP
The main direct benefits of CPAP are improved oxygenation, decreased respiratory effort, and decrease in left ventricular preload and afterload.
A recent study showed that with 2 weeks of CPAP usage for patients with CHF, pulmonary function was improved.

## Slide 22: Goals of CPAP
Elimination of dyspnea
Reduced respiratory rate
Reduced heart rate
Increased SpO2
Stabilized blood pressure

## Slide 23: Important
Once a patient is started on CPAP, only remove treatment if the patient deteriorates or under medical control direction.
Call ahead to ER and inform them that patient is on CPAP, do not just unhook the patient and leave.

## Slide 24: Summary
CPAP has been found to be as affective or more affective than the conventional pharmacological interventions.
CPAP is now being used as a part of GMVEMSC protocol