## Slide 1: MARCS Radio System Training Part 1: Transition

## Slide 2: TRAINING AGENDA
Why We’re Changing
Current Radio Systems
MARCS
Emergency Buttons
Transition Template
Transition Process
Summary

## Slide 3
Why we are changing

## Slide 4: WHY WE’RE CHANGING
Both Dayton and Montgomery County Trunked Radio Systems (TRS) are at end of life
Digital system improvements
MARCS offers vast interoperability
Montgomery County digital system going live in August, 2016 with ten radio towers

## Slide 5
Current radio systems

## Slide 6: CURRENT RADIO SYSTEMS
Primarily use two “trunked” (i.e., computer-controlled) radio systems:
  City of Dayton Trunked Radio System (TRS)
  Montgomery County Trunked Radio System (TRS)

## Slide 7: Current Montgomery County Fire Template

## Slide 8: Current Montgomery County Fire Template
CH | FIRE DEPT ZONE 1 | HOSPITAL ZONE 2 | FIRE DEPT ZONE 3 | ZONE 4 | ZONE 5 | ZONE 6 | ZONE 7 | ZONE 8 | INTEROP ZONE 9 | REGIONAL ZONE 10
1 | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP | FIRE DISP
2 | USER DEFINED | CMC* | USER DEFINED | Operations 42 | Operations 52* | Operations 62 | Operations 72 | Operations 82 | LE 1 | Operations 102
3 |  | MVH* |  | Operations 43 | Operations 53* | Operations 63 | Operations 73 | Operations 83 | LE 2 | Operations 103
4 |  | MVH S |  | Operations 44 | Operations 54* | Operations 64 * | Operations 74 | Operations 84 | LE 3 | Operations 104
5 |  | GSH* |  | Operations 45 | Operations 55* | Operations 65 * | Operations 75 | Operations 85 | LE 4 | Operations 105
6 |  | GVH* |  | Operations 46 | Operations 56* | Operations 66 | Operations 76 | Operations 86 | I-OP 1 | Operations 106
7 |  | KMC* |  | Operations 47 | Operations 57* | Operations 67 | Operations 77 | Operations 87 | I-OP 2 | MUTUAL AID
8 |  | SMC |  | Operations 48 | Operations 58* | Operations 68 | Operations 78 | Operations 88 | I-OP 3 | R3 RST
9 |  | SVH |  | Operations 49 | Operations 59* | Operations 69 | Operations 79 | Operations 89 | I-OP 4 | MCOEM
10 |  | WPMC* |  | Medic 4 Alpha | Medic 5 Alpha* | Medic 6 Alpha | Medic 7 Alpha | Medic 8 Alpha | COMMON | CORONER
11 |  | VA* |  | Medic 4 Bravo | Medic 5 Bravo* | Medic 6 Bravo | Medic 7 Bravo | Medic 8 Bravo | 8 CALL 90+ | MARCS SO57
12 |  | 8 TAC 92D A1+ |  | Medic 4 Charlie | Medic 5 Charlie* | Medic 6 Charlie | Medic 7 Charlie | Medic 8 Charlie | 8 TAC 91+ | MARCS SELECT
13 |  | 8 TAC 94D A2+ |  | Huber FD Disp | Dayton FD Disp* | Kettering FD Disp | Englewood FD Disp | County RDC 1 | 8 TAC 92+ | UHF
14 |  | HEALTH |  | Vandalia FD Disp | Airport FD (DOA)* | Oakwood FD Disp * | Moraine FD Disp | County RDC 2 | 8 TAC 93+ | REGROUP (MC)
15 |  | HOSP NET |  | DISP CEN DAY800* | DFD MC800 | Wash Twp FD Disp | W Carrol FD Disp | RDC DAY800* | 8 TAC 94+ | REGROUP (DAY)*
16 | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+ | FD Simplex+

## Slide 9: RADIO TEMPLATE
All Zones of current Montgomery County Fire Interoperability Template have Dispatch at the top and FD Simplex at the bottom
  Can always find dispatch by rotating all the way up to “1” and find FD Simplex by rotating all the way down to “16”

## Slide 10
Marcs

## Slide 11: MARCS
MARCS:
  Ohio Multi-Agency Radio Communication System
  Statewide trunked digital radio system for state, local, and federal public safety and first responder entities

## Slide 12: MARCS
MARCS - Multi-Agency Radio Communication System
  “SYSTEM OF SYSTEMS”
  Operated by state of Ohio - in conjunction with local agencies
  Montgomery County building all new Digital Trunked Radio System
  As with many other counties (Franklin, Butler, Warren, Hamilton, Cuyahoga, etc.), new Montgomery County TRS will become a system within MARCS

## Slide 13: MARCS “SYSTEM OF SYSTEMS”
Dedicated to providing Ohio's first responders and public safety providers with state-of-the-art wireless digital communications, and to promote interoperability, in order to save lives and maximize effectiveness in both normal operations and emergency situations.

## Slide 14: MARCS
MARCS Facts:
  700/800 MHz radio network using state-of-the-art trunked technology to provide digital clarity
  Throughout Ohio and 10 mile radius outside Ohio
  Maximum statewide interoperability
  Currently over 47,500 voice units on MARCS representing over 1200 public safety/public service agencies statewide
    including local, state, and federal agencies

## Slide 15: MARCS BENEFITS
Interoperability:
  Fire
  EMS
  LE
  Public Health
  Hospitals
  Public Works
  Others

## Slide 16: MARCS BENEFITS
Vast interoperability:
  Neighboring counties
    Greene
    Butler
    Warren
    Clark (some agencies)
    Miami (Fall/Winter 2016)
    Darke (considering)
  Distant counties
    Emergency Response System activation
      Giving
      Receiving

## Slide 17: MARCS Coverage
MARCS-IP Coverage Map

## Slide 18: MARCS SYSTEMS TERMINOLOGY
All the same:
  MARCS IP
  P-25
  MARCS Digital

## Slide 19
Emergency buttons

## Slide 20: ORANGE BUTTON - EMERGENCY BUTTON
What Orange Buttons do once we move to MARCS

## Slide 21: ORANGE BUTTON - EMERGENCY BUTTON
ORANGE BUTTON - EMERGENCY BUTTON
  Tactical - Once activated you will stay on the talkgroup you were on when the emergency button was hit.
  The dispatcher will see on their console the radio alias for which radio activated the emergency.
    The dispatch center that sees the emergency activation may not necessarily be “your” dispatch center.
  This talkgroup becomes a high priority talkgroup – meaning it receives priority in the queue for channel assignment from the master controller
  User must be on a trunked radio system for this to work.
    Will not work while using simplex or any conventional channel. Radio will “Bonk” if you hit the orange button.

## Slide 22: ORANGE BUTTON - EMERGENCY BUTTON
  If you are on a Hospital talkgroup and you hit the emergency button your radio will revert to your primary dispatch talkgroup
    Dispatch centers do not have the hospital talkgroups programmed in their consoles.

## Slide 23: ORANGE BUTTON – EVACUATION TONE
ORANGE BUTTON - EVACUATION TONE
  Press and hold the PTT, then press and release the orange button
  A high/low tone will be emitted on all other radios using the same talkgroup.
  The tone will stop once the PTT is released
  This will not work on the MARCS digital system

## Slide 24: RADIO SYSTEM
Radio System Failure
  Coverage problem/Out of range signal
    Switch to FD Simplex
    Note: SOPs should require someone outside a structure to monitor FD Simplex

## Slide 25: Montgomery County Transition Template

## Slide 26: TRANSITION TEMPLATES
The transition template is a radio template with talkgroups programmed for the new P25 Trunked Radio System and talkgroups for the existing analog Trunked Radio System
Radios need to be programmed with the “Transition Template” no later than August 1
  Responsibility of each agency
Radios will be programmed with the new talkgroups in Zones 1-23 or in some radios Zones 1-32

## Slide 27: TRANSITION TEMPLATES
ZONE A - I
  First nine zones of current fire template
  We will use Zones A-I until the August Cut-Over
  Continue to operate as usual using the talkgroups in these zones
  Zone 10 removed to make room for additional programming
  Old zones lettered not numbered to avoid confusing old and new systems
ZONE 1 - 23
  The new talkgroups will be in Zones 1 – 23 new MARCS template
  Some agencies are putting in full final template and their new talkgroups will be in Zones 1-32
  New Zones are numeric

## Slide 28: RADIO TEMPLATE
All Lettered Zones of Transition Template have Dispatch at the top and FD Simplex at the bottom
  Can find dispatch by rotating all the way up to “1” and find FD Simplex by rotating all the way down to “16”
SOME numbered Zones of Transition Template have Dispatch at the top and FD Simplex at the bottom
  NOT ALL!

## Slide 29: TRANSITION TEMPLATE – “OLD” STUFF- use until August Cut-Over

## Slide 30: TRANSITION TEMPLATE
Begin using these Zones 1-23 or 1-32 at Cut-Over (Mid-August 2016)

## Slide 31: TRANSITION TEMPLATE
Zones 1 and 2
  User defined talkgroup assignments (similar to today's Z1 and Z3)
Z3 Hosp
  Additional user defined zone
  Can be used for additional talkgroups for normal use
  Preferred/recommended to use this as primary transport hospital zone
  With expansion of emergency care centers (GSH N, KHN Franklin, etc.), this allows for departments to decide what primary transport hospitals they want in this zone

## Slide 32: TRANSITION TEMPLATE
  Zone 4, 6 & 7
    57 FD40, 57FD60 and 57FD70
      All Montgomery TGs will be preceded by 57 (Ohio county identifier)
    Shared talkgroups similar to today's template
      Ops 42 – 49, 62 – 69 and 72 – 79
      Med 4A/4B/4C, 6A/6B/6C, and 7A/7B/7C
    OPS 49/69/79 encrypted with ADP shared encryption
  Zones 8 – 9
    57 FD80 – 57 FD90
    Shared talkgroups for departments dispatched by RDC
    OPS 80 and 90 encrypted with ADP shared encryption
    Dayton FD going to 90
    DOA Fire is now in Zone 9
    RDC EMS TGs will become Ops 8A/8B/8C/8D and 9A/9B/9C/9D instead of “Med”

## Slide 33: TRANSITION TEMPLATE

## Slide 34: TRANSITION TEMPLATES – NEW STUFF
  Zones 5 & 10
  Zone 5
    R3HOSP1
    Hospital zone that includes Region 3 Hospital ER calling channels for facilities in Montgomery County
  Zone 10
    R3HOSP2
    Hospital zone that includes ER calling channels for facilities in the Region 3 area (except Montgomery County)
  57ED1, 57ED2, and R3ED3
    Hospital Expansion TGs

## Slide 35: MCI TALK GROUPS
During an MCI, current system of repeatedly changing to different hospital Talk Groups, entering encodes each time is time-consuming and ineffective
  Also causes fragmented communications
Solution: MCI Talk Groups
  GDAHA hospitals purchasing separate radios specifically for this purpose
  No need to switch TGs:
    Transport Officer simply notifies one hospital
    After acknowledgement, notifies the next
  All hospitals have a “common operating picture”

## Slide 36: TRANSITION TEMPLATES – NEW STUFF
  MCI TGs
    HSR3-MCI in both Zone 5 and Zone 10
    HSR6-MCI in Zone 10
HSR3-MCI TG will eventually reach all Region 3 hospitals
HSR6-MCI TG will reach all Region 6 hospitals
    Can be patched together by MARCS-allowed dispatch centers (PSAPs)

## Slide 37: TRANSITION TEMPLATE

## Slide 38: TRANSITION TEMPLATES – NEW STUFF
    Zone 11
      57CNTYWDE TGs
        County-wide event use talkgroups
        Similar to current I-OPS 1, 2, 3, and 4
        More of them to eliminate separate special event talkgroups
      LE talkgroups included with purpose similar to our current LE talkgroups in the interop zone
      MCOEM, Coroner, Animal Resource Center, MC Jail, RTA Supervisor, and Five Rivers Metro Police
    Important note: LE has different meanings depending on context
      MARCS LE TGs are local event
      The 57 LE TGs are Law Enforcement

## Slide 39: TRANSITION TEMPLATE
      Zone 12
        57PD PSAPS
        Lists primary talkgroups for each of the police Public Safety Answering Points (PSAPs)
        Gives capability for FD crews to contact PD dispatch centers directly
        Only one talkgroup per PSAP
      Zone 13
        8TAC I/O (zone display)
        800 Mhz national interoperability stand alone repeaters
          Conventional channel; not on trunked system
        Includes (5) 8CALL/TAC repeaters
        Includes (3) 800Mhz repeaters for use in Montgomery County

## Slide 40: TRANSITION TEMPLATE

## Slide 41: TRANSITION TEMPLATES – NEW STUFF
      MARCS interoperability zones
        Talkgroups designed by MARCS for interoperability
        Added:
          SW ROAD TAC Talkgroup designed for use by public works departments when working together on a regional response (snow/debris removal)
          SW TRANSPORT Talkgroup designed for use by transportation agencies when working on mass transport issues (evacuations/large event transportation plans).

## Slide 42: TRANSITION TEMPLATE
ECOMMs
Used as tactical (“ops”) channels during emergency incidents
Available to all MARCS users
  Especially beneficial in interdisciplinary incidents (e.g., an incident with public health on scene)
Must request an ECOMM through MARCS Help Desk (HLPDSK TG, or by phone)
  Reach MARCS Helpdesk 24/7 @ 1-866-OH-MARCS (1-866-646-2727)
Be prepared to give name and phone number, as well as an estimate of how long ECOMM will be in use (hours, days, week, etc.), and authority for request (IC)

## Slide 43: TRANSITION TEMPLATE

## Slide 44: TRANSITION TEMPLATE
      Zones 16 & 17
        9 FIRE A & 9 FIRE B
        Butler County fire interoperability zones
      Zone 18
        12 FIRE 1
        Clark County fire interoperability zone
      Zone 19 & 20
        29FIRE 1 & 29FIRE 2
        Greene County fire interoperability zones

## Slide 45: TRANSITION TEMPLATES – NEW STUFF
      Zone 21
        55FIRE
        Miami County fire interoperability zone.
      Zone22 & 23
        83 FIRE A & 83 FIRE B
        Warren County fire interoperability zones

## Slide 46: TRANSITION TEMPLATE

## Slide 47
Transition Process

## Slide 48: TRANSITION PROCESS
Coverage testing of new system will take place in the beginning of August 2016
System cut-over will be in Mid-August with entities changing over on the following plan:
  Day 1 – All hospitals, VA, UD and Sinclair and public work entities
  Day 2 – Huber Heights, Englewood and Vandalia
  Day 3 – Centerville, Kettering, Moraine and Oakwood
  Day 4 – RDC customers including Dayton Airport
  Day 5 – Contingency day

## Slide 49: TRANSITION PROCESS
Not just “turn one on, turn the other off”
Cannot reprogram hundreds of radios “instantly”
  All radios need to have both old and new systems by August
Period of time when parts of both systems on
To provide for that, MVFEA Communications Committee developed the “Transition Template”

## Slide 50: TRANSITION PROCESS
Extensive support for radio technicians and dispatch centers during transition
Recommend all Dispatch Centers during Transition Week:
  Monitor both systems to extent possible and notify crews who are on wrong system
  Announce during EVERY dispatch whether assigned TG is on alphabet zone (old system) or numeric zone (new system)
Each department needs to ensure all personnel are notified and appropriately trained

## Slide 51: MUTUAL AID WITH DAYTON
Dayton will now be in Zone 9
  Dayton FD Ops will be 92-99
  Dayton Airport FD also in Zone 9

## Slide 52
Summary

## Slide 53: SUMMARY
Continue to use old system now
Use lettered zones until notified by your agency and dispatch center
During transition week, some agencies will be on new system, some on old
Recommend all dispatch centers make daily announcements during transition week
  Which agencies on old system; which on new
Roll call at time of switchover

## Slide 54: NEXT STEPS
Develop/program the final template
Provide further training and answer questions regarding the radio systems and transition process
Revise MVFEA Communications SOP
Develop MARCS Radio System Training for Montgomery County users

## Slide 55: CONTINUING EDUCATION
  EMS CE provided courtesy of Greater Miami Valley EMS Council
    Complete the accompanying quiz and you will automatically be issued a CE Certificate
  Fire Suppression CE provided courtesy of Miami Valley Fire/EMS Alliance
    Simply send an email stating you completed this training to: vtate@mvfea.com or jackiel@mvfea.com

## Slide 56: Questions?
For questions, contact Lt. David Andes, Dayton fire department, CITY OF DAYTON Radio System coordinator at 937-333-4521 or by email
David.andes@daytonohio.gov